Bread pore quantification by cryo-scanning electron microscopy images

Ursula Gonzales Barron and Francis Butler

Biosystems Engineering, University College Dublin, Earlsfort Terrace, Ireland

Microstructural knowledge of food products is critical if properties are to be controlled properly since there is a causal connection between structure and functionality. The microstructure of bread determines the appearance, texture, taste perception and stability of the final product and it can give a visual explanation as to why bread of similar chemical composition has measurable different textures. The objective of this work was to quantify the bread pore microstructure by using cryo-scanning electron microscopy (cryo-SEM) to obtain actual crumb feature values and to compare them to similiar features extracted from macroscopic images (using a digital camera imaging system).

White bread samples of approximately 4×4×3 mm3 were carefully cut and observed at 10 kV and -130°C in a cryo-scanning electron microscope, and digitised in grey-level images of 1024×800 pixels. The levels of magnification (50×, 75×, 100× and 150×) were chosen in such a way that the images could encompass a number of gas cells so that a more realistic estimation of the void fraction could be undertaken. Prior to the acquisition of the SEM micrographs, images were obtained with a high-resolution digital camera (1 pixel line ~ 0.02987 mm) from the same four middle slices of the four bread loaves that were used for the SEM. The images represented 50×50 mm of the sample (1674×1674 pixels).

The cryo-SEM images of bread crumb (n=80) showed that bread is a two-phase system of randomly dispersed cells or cavities that occupy a high volume fraction (~ 0.75 void fraction) in a solid matrix. These cavities were, to a great extent, interconnected, in contrast to what the macroscopical (camera) images would normally suggest. Crumb cells were as small as 10 μm of equivalent diameter, though some tiny bubbles (10 – 80 μm) were mostly located within the cell walls. The intercellular distance or cell wall thickness was on average 60 μm although its range was considerable (10 – 300 μm). Thus, whereas the void fraction is underestimated in the results from the camera images (~ 0.45), the intercellular distance is overestimated (~ 0.86 mm). The gas cells observed in the micrographs had on average a more compact (compactness = 0.800) and less elongated shape (aspect ratio = 1.494) than the ones imaged by the camera (compactness = 0.780, aspect ratio = 1.617).

Preference: oral presentation and formal peer reviewing.

# Footnotes

Corresponding author. E-mail address: f.butler@ucd.ie