Task Hazard Analysis #158 Storm Damage Surveys Revised 20070517

| BASIC STEPS | HAZARDS (Known or foreseeable) | CONTROL MEASURES | PERSONAL PROTECTIVE EQUIPMENT | TRAINING |
| --- | --- | --- | --- | --- |
| Storm Damage Site visits involve: |  |  |  |  |
| Pre-trip planning Weather forecasts Determination of accessibility/safety of site Setting out and “Working Alone” | Inclement weather, including the possibility of more severe storms which may affect your ability to travel to or from the site or conduct your work at the site. Impeded/damaged transportation routes: airports and roadways, and to property in and around the affected area. Working Alone | Document safe work procedures for Storm Damage Surveys and ensure employees are familiar with them. | Provide PPE and clothing appropriate for conditions and task: This may include: CSA approved hard hat Hearing protection with attenuation of at least 29 dBA CSA approved safety glasses, goggles or face shield CSA approved safety work boots Work gloves. First aid kit. Review SWP, and manufacturers recommendations for PPE in Storm Survey Kit for details | Ensure employees receive mandatory training in Storm Damage Surveys and are observed for competence. Further training may include, but is not limited to: Knowledge of the departmental Safety Check in Directive Advanced driver training and collision avoidance Use and maintenance of PPE Wild animal avoidance |
| General travel to and from site and while at site Driving Aircraft | Hazards listed in THA’s for driving, fixed wing or helicopter travel. Unfamiliarity with operation of transportation (rental vehicles) Flat tire, running out of fuel (gas or diesel) or other vehicle failure Unfamiliar or lesser maintained roads, including grid roads. Unusual objects on roadway (pedestrians, animals, debris, parked or slow moving vehicles including emergency vehicles) Deteriorating local safety conditions |  |  |  |
| Performing the storm survey | Insufficient or excess illumination Lack of situational awareness – weather related Lack of situational awareness – not weather related Ground (slippery or unstable ground, tripping over debris or into holes while walking about) Pulled muscles and sprains Noise (hearing damage) Dust Chemical/biological exposure (industrial, agricultural or household chemicals, manure or sewage) Debris - Injury or death from encounters with falling, leaning, hanging, sharp, pointed or hidden debris (such as buildings, trees, branches, nails, screws, wires, broken glass or wood and jagged metal, either exposed or hidden in brush, grass or unstable piles of debris) Fire or explosions (gas leaks) Electrocution from contact with exposed “live” overhead or structural wiring (wires suspended overhead, hanging, touching or laying on the ground or hidden in grass, piles of debris or standing water) Animals (domestic or wild), rodents and Insects (mosquitoes, black flies, bees, wasps, hornets, ticks) that live in the ground, buildings, structures or in grass, brush or trees Drowning Potentially traumatized and/or hostile individuals Fatigue due to hunger, dehydration, heat, cold or overwork |  |  |  |

# Other Related Documents / Resources

- http://infolane.ec.gc.ca/%7Ehr/OSH/hazards_e.html

- http://infolane.ec.gc.ca/%7Ehr/OSH/arp_e.html

- Updates to this THA must also be reflected in the associated Safe Work Procedure (SWP)

| Manager’s name & signature / Date |  | Employee’s name & signature / Date |
| --- | --- | --- |